## Slide 1
R1 (Equilibrium reactor): The flowsheet utilizes an equilibrium reactor for the esterification reaction. A near-complete conversion of Benzoic Acid has been observed in the equilibrium reactor, yielding a large k, which we will correct once we obtain the detailed kinetics.
Since it's Equilibrium Reactor, temperature & pressure are taken directly from the feed stream(s) entering in it, implying Temperature is 25 °C and Pressure is 1 bar.
Benzoic Acid + Methanol → Methyl Benzoate + H2O
  Reactor (T & P)

## Slide 2
Near Atmospheric Pressure (1 bar)
The primary reason is that this pressure is cost-effective equipment-wise. Another important reason is that no azeotropes are formed at this pressure.
The Molar Ratio (Methanol : Benz_A = 16.59 : 2.7)
High Excess of Methanol: The Primary purpose is to drive equilibrium toward ester formation. This ratio enabled a large amount of water in the product. In our process, water helped in the energy-efficient separation of methanol.
Source: Roberts & Urey (1938)1
Moderate Temperature (25°C)
Warm enough to maintain reasonable reaction rates Cool enough to prevent excessive side reactions. And at this temperature all except the acids are in liquid phase. The excess methanol well encompasses the requirement of solvent for Benzoic Acid (as per solubility data).
  Operating Conditions for Reactor:

## Slide 3
Distillation Column Sequencing:
  Distillation Column Design & Sequencing

## Slide 4
Methanol + Water
Methyl Benzoate + Benzoic Acid + Phthalic Acid
C1
Distillation Column Sequencing:
Methanol
Water
C2
Methyl Benzoate
Benzoic Acid + Phthalic Acid
C3
Benzoic Acid
Phthalic Acid
C4
  Distillation Column Design & Sequencing

## Slide 5
Distillation Column Design:
C1 | C2 | C3 | C4
For 99.9% water recovery: | For 99.99% methanol recovery & 99.9% water recovery: | For 99.7% Methyl Benzoate recovery: | For 99.9% Benzoic Acid recovery:
No of Trays: 20 Feed Stage: 11 Reflux Ratio: 0.018697 Reboiler Duty: 22531.7 kW Condenser Duty: -17596.4 kW | No of Trays: 20 Feed Stage: 14 Reflux Ratio: 1.7256 Reboiler Duty: 38339.7 kW Condenser Duty: -38109 kW | No of Trays: 20 Feed Stage: 11 Reflux Ratio: 0.3033 Reboiler Duty: 4291.45 kW Condenser Duty: -4435.88 kW | No of Trays: 20 Feed Stage: 10 Reflux Ratio: 1.19132 Reboiler Duty: 25 kW Condenser Duty: -18.84 kW
  Distillation Column DESIGN & Sequencing

## Slide 6
  Distillation Column Design & Sequencing: VLE checks
Column 2 Distillate:
Methanol = 0.9998
Water = 0.0002
Temp = 64.2 °C
Tsat = 64.26 °C

## Slide 7
  Distillation Column Design & Sequencing: VLE checks
Column 2 Bottom:
Methanol = 0.001
Water = 0.999
Temp = 104.34 °C
Tsat = 104.44 °C

## Slide 8
  Distillation Column Design & Sequencing: VLE checks
MEB = 0.99
Water = 0.01
Temp = 190 °C
Tsat = 191.32°C
Column 3 Distillate:

## Slide 9
  Distillation Column Design & Sequencing: VLE checks
PTH = 0.6
MEB = 0.4
Temp = 247 °C
Tsat = 247.24°C
Column 3 Bottom:

## Slide 10
  Operating Conditions for Distillation Columns
Column | Condensor Pressure | Condensor Temperature | Reboiler Pressure | Reboiler Temperature
C1 | 1 bar | 66.6 °C | 1.2 bar | 198.1 °C
C2 | 1 bar | 64.2 °C | 1.2 bar | 104.4 °C
C3 | 1 bar | 190.8 °C | 1.2 bar | 247.1 °C
C4 | 1 bar | 200.11 °C | 1.2 bar | 331.45 °C

## Slide 11
Column 1
Design Specification | Component | Value
Mole Recovery | Water (D1) | 0.99
Vary | Limit (kW) | Value (kW)
Reboiler Duty | 0.01-107 | 22531.659
  Design Specifications
Methanol + Water
Methyl Benzoate + Benzoic Acid + Phthalic Acid

## Slide 12
Design Specification | Component | Value
Mole Recovery | Methanol (D2) | 0.9998
Mole Recovery | Water (B2) | 0.999
Vary | Limit | Value
Reflux Ratio | 0.01-100 | 1.726
Reboiler Duty | 0.01-106 (kW) | 38339.74 (kW)
  Design Specifications
Methanol
Water
Column 2

## Slide 13
Design Specification | Component | Value
Mole Recovery | MEB (D3) | 0.9975
Vary | Limit | Value
Reflux Ratio | 0.0001-100 | 0.30334847
  Design Specifications
Methyl Benzoate
Benzoic Acid + Phthalic Acid
Column 3

## Slide 14
Design Specification | Component | Value
Mole Recovery | Phthalic Acid (B4) | 0.999
Vary | Limit | Value
Reflux Ratio | 0.001-100 | 1.19131864
  Design Specifications
Column 4
Benzoic Acid
Phthalic Acid

## Slide 15
  Temperature Profiles for Distillation Columns

## Slide 16
  Temperature Profiles for Distillation Columns

## Slide 17
  Temperature Profiles for Distillation Columns

## Slide 18
  Temperature Profiles for Distillation Columns

## Slide 19: ChE 453: Capstone Project
Mid Semester Presentation
Group 4

## Slide 20
  Rationale for choice of product (Methyl Benzoate)
Methyl Benzoate selected due to high demand in fragrance, flavor, and pharmaceutical industries.​
Exhibits 6% CAGR growth (2024–2032), market projected to reach USD 2,260 million by 2032.​
Multi-purpose applications: solvent, agrochemicals, intermediates, and antifungal uses.​
High value product compared to raw feedstocks (Methanol & Benzoic Acid).​
https://dataintelo.com/report/global-methyl-benzoate-market

## Slide 21
  Product Purity Considerations
Target: High-purity methyl benzoate to meet industrial-grade standards (~99%).
Impurities: Trace phthalic acid (in Benzoic Acid)
UNIQUAC thermodynamic model ensures accurate phase behavior and separation efficiency.
No azeotrope formation → simplifies purification & lowers separation costs.

## Slide 22
  Feedstock Quality
Methanol: 16.95 moles, low cost (USD 345–370/MT), widely available.
Benzoic Acid: 2.7 moles with 0.5% phthalic acid impurity; quality feed ensures reaction efficiency.
Stable global supply: both feedstocks projected for steady market growth (Methanol CAGR 4.7%, Benzoic Acid CAGR 5.3%).
Selection balances cost efficiency with required chemical reactivity.
Molar Ratio of Methanol to Benzoic Acid is taken as 6.27 for optimum utility. Source: Roberts & Urey (1938)1

## Slide 23
  Feedstock Quality
Methanol Market: CAGR (4.7%, 2025-2034)
Benzoic Acid Market: CAGR (5.3%, 2024-2033)
https://www.polarismarketresearch.com/industry-analysis/methanol-market
https://dimensionmarketresearch.com/report/benzoic-acid-market

## Slide 24
  Input-Output Economic Feasibility
 | Benzoic Acid | Methanol | Methyl Benzoate | 
 |  |  |  | Molar Efficiency
MW(gm/mole) | 122.12 | 32.04 | 136.15 | 0.9
Mass(kg) | 996.61 | 1641.02 |  | 
Raw Mass(kg) | 1001.62 | 1641.02 | 1000.00 | Methanol Purity
Mole/day | 8160.91 | 51217.79 | 7344.82 | 1
Excess Mole | 0.00 | 43056.88 |  | 
Raw Mass(MTon) | 1.00161809 | 1.641018026 | 1.00 | Benzoic Acid Purity
Cost(USD/MT) | 1010.00 | 370.00 | 2200.00 | 0.995
UnReacted Mole | 816.09 | 43872.97 |  | 
UnReacted Mass(Mton) | 0.10 | 1.41 |  | MeOH:BnZ_A
Total Cost(USD) | 1011.634271 | 607.1766696 | 2199.99 | 1.6466
Total Input Cost (USD) |  |  | 1618.81 | 
Excess Reactant Cost (USD) |  |  | 620.76 | 
Total Output Cost (USD) |  |  | 2199.99 | 
Net Profit (USD) |  |  | 1201.94 | 
Profit (x) |  |  | 1.204295709 | 
Source: Roberts & Urey (1938)1

## Slide 25
  Thermodynamic model validation
NRTL
PENG-ROB
UNIQUAC
UNIQUAC IS THE BEST MODEL, AS IT BEST FITS THE DATA!

## Slide 26
  Thermodynamic Parameters
Estimated the rest of parameters of UNIQUAC model using UNIFAC
Component i | Component j | AIJ | AJI | BIJ | BJI | CIJ | CJI | DIJ | DJI | Tlower (C) | Tupper (C)
BENZA | WATER | -61.6506 | -7.3661 | 2424.886 | 1073.019 | 9.4538 | 0.4699 | 0 | 0 | 64 | 115.5
BENZA | METH | 0 | 0 | -19.163 | 210.75 | 0 | 0 | 0 | 0 | 20 | 40
WATER | METH | 0.6437 | -1.0662 | -322.131 | 432.8785 | 0 | 0 | 0 | 0 | 24.99 | 100
MEB | BENZA | 0 | 0 | -249.979 | 151.4731 | 0 | 0 | 0 | 0 | 25 | 25
MEB | WATER | 0 | 0 | -421.25 | -165.418 | 0 | 0 | 0 | 0 | 25 | 25
MEB | METH | 0 | 0 | -385.159 | 48.13078 | 0 | 0 | 0 | 0 | 25 | 25
MEB | PTH | 0 | 0 | -297.173 | 128.2428 | 0 | 0 | 0 | 0 | 25 | 25
BENZA | PTH | 0 | 0 | -36.1404 | 19.82719 | 0 | 0 | 0 | 0 | 25 | 25
WATER | PTH | 0 | 0 | -261.525 | 104.1981 | 0 | 0 | 0 | 0 | 25 | 25
METH | PTH | 0 | 0 | 188.7415 | -303.671 | 0 | 0 | 0 | 0 | 25 | 25

## Slide 27
Section 2
Block diagram and rationale behind the process synthesis (covering elements like feed purification, product separation, recycles etc.)
Material balance

## Slide 28
  Block diagram

## Slide 29
Fresh Benzoic Acid Feed: Solid reactant input (2.7 mol ratio); provides core material for esterification, directly fed to the mixer M1 for slurry creation.
Fresh Methanol Feed: Excess reactant (16.59 mol ratio); acts as solvent and equilibrium shifter, can be recycled to sustain high conversion and reduce costs.
B5 Heater: Preheats feed stream to maintain desired reaction temperature i.e., 298.15 K.
M1 Mixer: Blends benzoic acid and methanol into slurry; handles solid dissolution for phase-compatible reactor feed, ensures efficient reaction start.
  Block diagram
Mass flows of reactants taken initially :-
Methanol: 54303 kg/hr, Benzoic acid: 32851 kg/hr
Mass of products formed:-
Methyl benzoate: 36529 kg/hr, Water: 48.5 kg/hr
*The above have been taken based on ratios provided in the original literature, as well as enabling a significant profit margin. Also, we have kept ease of verification in mind

## Slide 30
R1 Equilibrium Reactor: Site of esterification (Benzoic Acid + Methanol → Methyl Benzoate + H₂O); models' reversible kinetics with such excess ratio yields very large k indicating near-complete conversion.
C1 Distillation Column: Initial split of R1 effluent to D1 (methanol/water overhead) and B1 (MEB/acids bottoms); 20 trays, low reflux for energy-efficient light removal based on volatility differences.
  Block diagram

## Slide 31
C2 Distillation Column: Purifies D1 into D2 (methanol distillate, 99.99% recovery) and B2 (water bottoms); 20 trays.
  Block diagram

## Slide 32
C3 Distillation Column: Isolates D3 (MEB distillate, 99.7% recovery) from B3 (acids bottoms); 20 trays exploit MEB volatility for product purification with minimal energy (low reflux).
  Block diagram

## Slide 33
C4 Distillation Column: Recovers D4 (benzoic acid distillate, 99.9%) from B4 (phthalic acid purge bottoms); 20 trays close acid loop, removes impurities to prevent buildup.
  Block diagram

## Slide 34
Column C1 | Mass In (S1) | Mass Out(B1) | Mass Out(D1) | Mass Out total
Methyl Benzoate | 36622.21057 | 36620.80996 | 1.400610149 | 36622.21057
Benzoic Acid | 1.996230958 | 1.996230958 | 2.47E-24 | 2.00E+00
Water | 4845.815842 | 48.45815348 | 4797.357689 | 4845.815842
Methanol | 45692.64392 | 0.017089908 | 45692.62683 | 45692.64392
Phthalic Acid | 166.13324 | 166.13324 | 1.97E-39 | 1.66E+02
TOTAL | 87328.7998 |  |  | 87328.7998
Column C2 | Mass In (D1) | Mass Out(B2) | Mass Out(D2) | Mass Out total
Methyl Benzoate | 1.400610149 | 1.400610149 | 0 | 1.400610149
Benzoic Acid | 2.47E-24 | 0 | 0 | 0
Water | 4797.357689 | 4792.560331 | 4.797357688 | 4797.357689
Methanol | 45692.62683 | 9.138525366 | 45683.4883 | 45692.62683
Phthalic Acid | 1.97E-39 | 0 | 0 | 0
TOTAL | 50491.38513 |  |  | 50491.38513
Column C1 | Heat In (kW) |  | Heat out (kW)
Feed (S1) | -141828.2926 | Distillate C1 (D1) | -113817.4079
Reboiler Duty C1 (Qr) | 22532 | Bottoms C1 (B1) | -23075.58014
Condenser Duty C1 (Qc) | -17596 |  | 
Total | -136892.2926 | Total | -136892.988
Column C2 | Heat In (kW) |  | Heat out (kW)
Distillate C1 (D1) | -113817.4079 | Distillate C2 (D2) | -92874.60482
Reboiler Duty C2 (Qr) | 38340 | Bottoms C2 (B2) | -20712.05695
Condenser Duty C2 (Qc) | -38109 |  | 
Total | -113586.4079 | Total | -113586.6618
Material and Energy Balance for Columns 1 and 2
  Material & Energy Balance

## Slide 35
Column C4 | Mass In (B3) | Mass Out(B4) | Mass Out(D4) | Mass Out total
Methyl Benzoate | 91.55202489 | 7.38E-07 | 91.55202415 | 9.16E+01
Benzoic Acid | 1.967318305 | 1.97E-05 | 1.967298588 | 1.97E+00
Water | 3.84E-15 | 0 | 0 | 0
Methanol | 9.13E-18 | 0 | 0 | 0
Phthalic Acid | 166.13324 | 165.9671068 | 0.16613324 | 166.13324
TOTAL | 259.6525832 |  |  | 259.6525832
Column C4 | Heat In (kW) |  | Heat out (kW)
Bottoms C3 (B3) | -253.7746107 | Distillate C4 (D4) | -58.29793905
Reboiler Duty C4 (Qr) | 25 | Bottoms C4 (B4) | -189.3194072
Condenser Duty C4 (Qc) | -19 |  | 
Total | -247.7746107 | Total | -247.6173463
Column C3 | Heat In (kW) |  | Heat out (kW)
Bottoms C1 (B1) | -23075.58014 | Distillate C3 (D3) | -22966.23687
Reboiler Duty C3 (Qr) | 4291 | Bottoms C3 (B3) | -253.7746107
Condenser Duty C3 (Qc) | -4436 |  | 
Total | -23220.58014 | Total | -23220.01149
Column C3 | Mass In (B1) | Mass Out(B3) | Mass Out(D3) | Mass Out total
Methyl Benzoate | 36620.80996 | 91.55202489 | 36529.2579 | 36620.80992
Benzoic Acid | 1.996230958 | 1.967318305 | 0.028912653 | 1.996230958
Water | 48.45815348 | 3.84E-15 | 48.45815344 | 4.85E+01
Methanol | 0.017089908 | 9.13E-18 | 0.017089908 | 1.71E-02
Phthalic Acid | 166.13324 | 166.13324 | 1.48E-12 | 1.66E+02
TOTAL | 36837.41467 |  |  | 36837.41464
Material and Energy Balance for Columns 3 and 4
  Material & Energy Balance

## Slide 36
  Block Diagram at a Glance

## Slide 37
  Cogeneration Unit & Turbines Operating conditions
HX1 Heat Exchanger: Preheats the incoming Rankine feed using water from C2 bottoms, reducing preheater duty
HX1
40 bar
10 bar
1 bar
3 bar

## Slide 38
CW Req | Energy | HPS Req | Energy | LPS Req | Energy
C1 Condenser | 120098. kW | C1 Reboiler | 120791 kW |  | 
C2 Condenser | 202084. kW |  |  | C2 Reboiler | 202132 kW
C3 Condenser | 4341 KW | C3 Reboiler | 4291 kW |  | 
C4 Condenser | 999 kW | C4 Reboiler | 1000 kW |  | 
Net | 327522 kW | Net | 126082 kW | Net | 202132 kW
Column | Condensor Pressure | Condensor Temperature | Reboiler Pressure | Reboiler Temperature
C1 | 1 bar | 66.6 °C | 1.2 bar | 198.1 °C
C2 | 1 bar | 64.2 °C | 1.2 bar | 104.4 °C
C3 | 1 bar | 190.8 °C | 1.2 bar | 247.1 °C
C4 | 1 bar | 200.11 °C | 1.2 bar | 331.45 °C
  Distillation Column Energy Requirements

## Slide 39
CW Loop Requirement
Unit | Net Requirements Cooling Water (kW)
Distillation | 327522
CW | 332324
Unit | Net Requirements High Pressure Steam (kW)
Distillation | 126082
Unit | Net Requirements Low Pressure Steam (kW)
Distillation | 202132
Distillation Unit Requirement
Stream | Energy Required | Mass Flow
HPSOUT | 126083 kW | 206574 kg/hr
LPSOUT | 205976 kW | 330828 kg/hr
Cooling Water | 332324 kW | 11441600 kg/hr
  Cogeneration Analysis: Requirement, Production, Deficit
CW Req | Energy
HEN4 | 772 KW
HEN5 | 16 KW
Rest | 331536 kW
Overall Requirements
Utility Requirements
*We have assumed that steam cannot be cooled beyond 100°C and cooling water cannot be heated beyond 40°C
CW Req | Energy | HPS Req | Energy | LPS Req | Energy
C1 Condenser | 120098. kW | C1 Reboiler | 120791 kW |  | 
C2 Condenser | 202084. kW |  |  | C2 Reboiler | 202132 kW
C3 Condenser | 4341 KW | C3 Reboiler | 4291 kW |  | 
C4 Condenser | 999 kW | C4 Reboiler | 1000 kW |  | 
Net | 327522 kW | Net | 126082 kW | Net | 202132 kW

## Slide 40
Stream | Electricity Produced (kW)
ELEC1 | 5.98 x 109
ELEC2 | 1.70 x 1010
ELEC3 | 1.14 x 1010
ELEC4 | 8.21 x 109
TOTAL | 4.26 x 1010
  Cogeneration Analysis: Net Electricity Generation
Mass flows of reactants taken initially :-
Methanol: 6964.89 kg/hr, Benzoic acid: 12016.40 kg/hr
Mass of products formed:-
Methyl benzoate: 13396.4 kg/hr
Total mass flow of water required in Rankine Cycle:-
Water: 1.62 x 1011 kg/hr (Hot Utility)
Total flow of Cooling Water required:-
Water:1.44 x 107 kg/hr (Cold Utility)
Methanol : Benzoic Acid : Methyl Benzoate : Hot Stream Utility : Cold Stream Utility
1 : 1.73 : 1.92 : 2.33 x 107 : 2.067 x 103

## Slide 41
  Cooling water loop
Notes: MBCWH AND MBCW cooling inlet and hot outlet water from cooling methyl benzoate
BACWH AND BACW cooling inlet and hot outlet water from cooling benzoic acid

## Slide 42
  Cooling water loop
Notes: MBCWH AND MBCW cooling inlet and hot outlet water from cooling methyl benzoate
BACWH AND BACW cooling inlet and hot outlet water from cooling benzoic acid

## Slide 43
  Cooling water loop
Design Spec | Manipulated variable | Target variable | Target value
1. | BACW Flow Fraction | BACWH Temperature | 40 °C
2. | MBCW Flow Fraction | MBCWH Temperature | 40 °C
3. | Total Mass Flow across MAKEUP | Total Fresh Cooling Water required | 0 tonne/hr

## Slide 44
  Reactor design and sequencing with detailed kinetics:
We are using a Plug Flow Reactor in our process with a conversion of 99.628%. Although the reaction is reversible, due to a lack of data (The value k in backward reaction was not provided and Keq calculation was not possible, as affirmed in the paper), we are considering our reaction only in the forward direction.

## Slide 45
  Reactor Design:
Flow Regime:
Average Velocity: 0.004328 m/s
Reynolds Number: 36960.81
Flow Regime: Turbulent (Re ≥ 4000)
The flow regime obtained in our reactor is turbulent which is consistent with standard industrial practices.
We usually operate PFR in turbulent regime due to following reasons:
Complete radial mixing (uniform temperature/concentration)
High heat transfer coefficients
Minimized axial dispersion (plug-flow approach)

## Slide 46
  Reactor Design:
Residence time:
The residence time obtained in our reactor is 2.56 hours, which is consistent with typical industrial ranges (1–5 hours) for plug flow reactors, especially for reactions requiring extended contact time.
In our system, we obtained a single-pass conversion of 58%. We implement reactant recycling to optimize resource utilization and minimize waste, allowing unreacted species to re-enter the reactor. This significantly boosts the overall conversion to 99.93%.

## Slide 47
  Results:
Composition Profile of Reactor:
Conclusion:
BENZA is the reactant, and it is being consumed along the reactor length.
MEB is the product, and it is being formed progressively as the reaction proceeds.
The monotonic decrease in BENZA and increase in MEB confirms that the reaction is proceeding forward without significant reverse reaction.
Fresh methanol feed rate = 61.3666 kmol/hr
Fresh benzoic acid feed rate = 57.812 kmol/hr Methyl Benzoate outlet flow rate = 57.77 kmol/hr

## Slide 48
  DETAILED HEAT EXCHANGER:
The Tubular Exchanger Manufacturers Association (TEMA) is an association of manufacturers of shell and tube heat exchangers. TEMA has established a set of construction standards for Shell and Tube Heat Exchangers.
E-Type shell is the more commonly used shell type, suitable for most duties and applications.
Tube diameter layout and pitch:
Tubes may range in diameter from 12.7 mm (0.5 in) to 50.8 mm (2 in), but 19.05 mm (0.75 in) and 25.4 mm (1 in) are the most common sizes.
Notes: "Good morning. I'll be presenting the detailed design of our *Shell and Tube Heat Exchanger*. The fundamental conceptual theory at play here is *convective heat transfer*
. We use this Shell and Tube Heat Exchanger to separate the hot and cold fluids, forcing heat to transfer efficiently across the metal tube walls. We chose the standard *TEMA E-Type shell* , which is the most common and cost-effective choice for general duties.

## Slide 49
  Shell & tube specification:
Tube Specifications:
Outer diameter: 20 mm
Inner diameter: 16 mm
Standard Length: 4.88 m
Area of tube (πDL) = 0.303324 m²
Number of tubes: 2425
Tin = 64.2 ℃, Tout = 35 ℃
Tmean = 49.6 ℃
Single pass
Mass Flow rate(kg/hr) = 382130.9
Mass Flow rate (kg/s) = 106.147
Mass Flow velocity = 217.815 kg/m²s
Linear velocity = 0.275 m/s
Pitch = 1.25 * outer diameter = 25 mm
The triangular arrangement allows more tubes in a given space.
In our system the number of tubes is 2425 so we’ll use triangular arrangement.
Shell Specifications:
Diameter = 1441 mm
Mass flow rate = 600000 kg/hr
Mass flow rate = 166.67 kg/s
Mass flow velocity = 2005.78 kg/m²s
Tin = 25 ℃
Tout = 40 ℃
Tmean = 32.5 ℃
Reynold’s number = 32004.6
Prandtl number = 6.2
Baffle cut = 25%
Notes: 2. *Performance Requirement:* The shell-side fluid is our process stream, which has a significant mass flow rate of *600,000 kilograms per hour. Our design must heat this stream from *$25^{\circ}C$ to $40^{\circ}C$*.
3. *Optimization:* This required a significant geometry: the final design contains *2,425 tubes, each with a standard length of **4.88 meters* and a $20 \text{ mm}$ outer diameter."

## Slide 50
  Heat exchanger INTERIOR DESIGN
Baffle types
Baffles are installed on the shell side to give a higher heat-transfer rate due to increased turbulence and to support the tubes thus reducing the chance of damage due to vibration.
Single segmental (this is the most common)
Baffles specification:
Number of baffles = 5
Baffle spacing(20 % of shell diameter) = 288.25 mm
Notes: To maximize heat exchange, we use *baffles* with a *25% cut. This forces the fluid into a turbulent, zigzag **cross-flow* pattern around the tubes, which greatly enhances the heat transfer rate.

## Slide 51
  Exchanger details:
Calculated:
Heat exchanger area = 735.3 m²
UA value = 625 kW/K
Aspen Results:
Heat exchanger area = 721.45 m²
UA value = 613.24 kW/K
The above calculated data matches with results obtained from Aspen:
Notes: Key Technical Result (Re):* The most important result is the calculated *Reynolds number* for the shell-side flow: *32,004.6. Since this is well above 10,000, we confirm **highly turbulent flow* is achieved.

## Slide 52
  Exchanger Design specifications (EDR) :

## Slide 53
Exchanger Design and Rating (EDR) :
EDR is a feature in Aspen used for the thermal and mechanical design and analysis of heat exchangers.
Tube results (All the properties of hot fluid, methanol):
Shell results (All the properties of cold fluid, water):
Notes: We can see the results of hot and cold fluid in tube and shell side and we can also see the value of temerature dependent properties

## Slide 54
  Tube material used:
Notes: Corrosion Resistance, Corrosion Resistance, he addition of 10% Nickel improves the mechanical strength

## Slide 55
  PINCH TECHNOLOGY

## Slide 56
  PINCH TECHNOLOGY
Stream | Condition | Flowrate (kg/s) | mCp (kW/C) | Tin | Tout | Qav (Kw)
1 (D2) | Hot | 106.15 | 341.89 | 64 | 35 | 9914.81
2 (D3) | Hot | 2.72 | 4.67 | 191 | 35 | 728.21
3 (D4) | Hot | 0.95 | 1.73 | 248 | 35 | 369.09
4 (LIQOUT) | Cold | 110.20 | 374.54 | 50 | 54 | 1498.16
5 (MIXOUT) | Cold | 110.20 | 348.69 | 25 | 50 | 8717.15
Methanol + Water
Methyl Benzoate + Benzoic Acid + Phthalic Acid
C1
Distillation Column Sequencing:
Methanol
Water
C2
Methyl Benzoate
Benzoic Acid + Phthalic Acid
C3
Benzoic Acid
Phthalic Acid
C4

## Slide 57
  PINCH TECHNOLOGY
Stream | Condition | Flowrate (kg/s) | mCp (kW/C) | Tin | Tout | Qav (Kw)
1 (D2) | Hot | 106.15 | 341.89 | 64 | 35 | 9914.81
2 (D3) | Hot | 2.72 | 4.67 | 191 | 35 | 728.21
3 (D4) | Hot | 0.95 | 1.73 | 248 | 35 | 369.09
4 (LIQOUT) | Cold | 110.20 | 374.54 | 50 | 54 | 1498.16
5 (MIXOUT) | Cold | 110.20 | 348.69 | 25 | 50 | 8717.15
1
9914.81
2
728.208
4
1498.16
5
8717.15
3
369.0864
CU
796.776
8717.15
1197.66
300.5
427.708
369.0864
Minimum number of Heat Exchangers = 5

## Slide 58
  PINCH TECHNOLOGY
Stream | 1 | 2 | 3 |  | 4 | 5 |  | 
mCp | 341.89 | 4.668 | 1.7328 |  | 374.54 | 348.686 | Kw/C | Energy (kW)
 |  |  |  | A |  |  |  | 98.769
 |  |  |  | B |  |  |  | 812.8
 |  |  |  | C |  |  |  | -104.996
 |  |  |  | D |  |  |  | -9.88
248
35
64
191
25
50
54
60
A, 98.769
B, 812.8
C, -104.996
D, -9.88
98.769
911.569
796.693
806.573
COLD UTILITY
HOT
UTILITY
No Pinch Detected!

## Slide 59
  PINCH TECHNOLOGY
HEN 1
HEN 2
HEN 4
HEN 3
HEN 5
4
5
2
1
3
60.496
53.2
50
35
25
50
54
126.81
191
64
248
126.81
248
248
50
54
35
35
35
50
Qc
Qc
Process Streams
Heat Exchangers
Cooling Utility
Connection directions

## Slide 60
  PINCH TECHNOLOGY

## Slide 61
We performed the sensitivity analysis to optimize the profit of our plant, in which we have included the below cost.
Reboiler Cost
Condenser Cost
Heater Cost
Tray Cost
Reactor Cost
Feed and Product Cost
  Techno-economic Analysis

## Slide 62
We performed the sensitivity analysis to optimize the profit of our plant, in which we have included the below cost.
Reboiler Cost
Condenser Cost
Heater Cost
Tray Cost
Reactor Cost
Feed and Product Cost
  Techno-economic Analysis

## Slide 63
We performed the sensitivity analysis to optimize the profit of our plant, in which we have included the below cost.
Reboiler Cost
Condenser Cost
Heater Cost
Tray Cost
Reactor Cost
Feed and Product Cost
  Techno-economic Analysis

## Slide 64
We performed the sensitivity analysis to optimize the profit of our plant, in which we have included the below cost.
Reboiler Cost
Condenser Cost
Heater Cost
Tray Cost
Reactor Cost
Feed and Product Cost
  Techno-economic Analysis

## Slide 65
We performed the sensitivity analysis to optimize the profit of our plant, in which we have included the below cost.
Reboiler Cost
Condenser Cost
Heater Cost
Tray Cost
Reactor Cost
Feed and Product Cost
  Techno-economic Analysis

## Slide 66
We performed the sensitivity analysis to optimize the profit of our plant, in which we have included the below cost.
Reboiler Cost
Condenser Cost
Heater Cost
Tray Cost
Reactor Cost
Feed and Product Cost
  Techno-economic Analysis

## Slide 67
  Techno-economic Analysis
Notes: Reactor cost v/s conversion tradeoff

## Slide 68
  Techno-economic Analysis
Notes: Methanol recovery increases fresh req reduces hence cost
Water recovery increases causing higher reboiler duty

## Slide 69
  Techno-economic Analysis
RESULTS (UNITS) | VALUES
TOTAL CAPITAL COST (TCC) ($) | 2.98 x 107
YEARLY OPERATING COST (YOC) ($) | 1.39 x 108
INPUT COST (RAW MATERIALS COST) ($) | 1.06 x 108
REVENUE (PRODUCT MARKET PRICE) ($) | 2.14 x 108
PAYBACK PERIOD (PBP) (YEARS) | 3
TOTAL ANNUALISED COST (TAC) ($) | 1.49 x 108
TOTAL ANNUAL PROFIT (TAP) ($) | 6.46 x 107
Notes: Enriching this stream cause higher reboiler duty

## Slide 70
Thanks!
Aaditya Amlan Panda (220007)
Abhijit Dalai (220030)
Adarsh Pal (220054)
Akash Kumar Gupta (220095)
Kushagra Tiwari (220574)
Saurabh Yadav (220991)
Snehil Tripathi (221071)
Tushar Verma (221147)
Presented by Group 4: